## Slide 1: Evaluation of WebAssembly IoT Runtimes on a ESP32 Microcontroller
Evaluation von WebAssembly IoT Runtimes auf einem ESP32 Microcontroller
Notes: Welcome to presentation
Glad to find a way to make it work

## Slide 2: Abstract
Run WebAssembly on the ESP32
Found runtime
WASM code runs on the ESP32 with decreased performance
Notes: Run WebAssembly on the ESP32
Find runtime
Design tests
Performance and system interfaces

## Slide 3: Outline
Background: ESP32 and WebAssembly
Methodology: Runtime and tests
Evaluation: Rest results and learnings

## Slide 4: Background

## Slide 5: The ESP32
Notes: Release in sept 2016
With bluetooth and wifi
More power than predecessor ESP8266 => encryption
Light bracelet alibaba annual meeting 2017
4MB flash and 520KB RAM
FreeRTOS

## Slide 6: WebAssembly adoption
Notes: For the web
Announced in 2015 cross browser consensus in 2017
Fix javascript performance inconsistency

## Slide 7: WebAssembly
Portable target for languages like C/C++ and Rust
Shipped in self-contained modules
Runs on stack machine
No web dependencies
Advantageous attributes for IoT
Structured control flow
Notes: Portable target
Module with functions, globals, imports, exports amongst others => encapsulation and sandboxing
Stack instead of registers => compact code since not paramters but stack
Best support on browsers, but new runtimes coming
Web => no trust, fast, universal, trasnittable
No Arbitrary jumps

## Slide 8: Structured control flow
instr ::= . . .
  | nop
  | unreachable
  | block resulttype instr∗ end
  | loop resulttype instr∗ end
  | if resulttype instr∗ else instr∗ end
  | br labelidx
  | br_if labelidx
  | br_table vec(labelidx) labelidx
  | return
  | call funcidx
  | call_indirect typeidx
Notes: WebAssmebly grammar
Interesting => Block, groups nested sequence, has implicit label
Br_if => conditional branch
Return => unconditional branch
Calling functions => taking from stack result to stack

## Slide 9: Methodology

## Slide 10: Running WebAssmbly
Notes: As metioned before, not feasible to use browser
Bytcode alliance nov 2019 => foundations to run WASM on multiple platforms in a secure way
WAMR doesn’t support FreeRTOS
Late 2019, 12x slower than native on refernce machines

## Slide 11: Testing setup
Main Program
WebAssembly
C-Code
Notes: WASM vs native

## Slide 12: Recursive: C++
uint32_t run(uint32_t n) { if (n < 2) { return n; } return run(n - 1) + run(n - 2); }
Notes: Fibonacci

## Slide 13: Recursive: WAT
(func $run (export "run") (type $t1) (param $p0 i32) (result i32) (block $B0 (br_if $B0 (i32.lt_u (local.get $p0) (i32.const 2))) (return (i32.add (call $run (i32.add (local.get $p0) (i32.const -1))) (call $run (i32.add (local.get $p0) (i32.const -2)))))) (local.get $p0))
Notes: WeAssembly text format
P0 argument

## Slide 14: Recursive: Comparison
(block $B0 (br_if $B0 (i32.lt_u (local.get $p0) (i32.const 2))) (return (i32.add (call $run (i32.add (local.get $p0) (i32.const -1))) (call $run (i32.add (local.get $p0) (i32.const -2)))))) (local.get $p0)
uint32_t run(uint32_t n) { if (n < 2) { return n; } return run(n - 1) + run(n - 2); }
Notes: Conditional branch

## Slide 15: Recursive: Comparison
(block $B0 (br_if $B0 (i32.lt_u (local.get $p0) (i32.const 2))) (return (i32.add (call $run (i32.add (local.get $p0) (i32.const -1))) (call $run (i32.add (local.get $p0) (i32.const -2)))))) (local.get $p0)
uint32_t run(uint32_t n) { if (n < 2) { return n; } return run(n - 1) + run(n - 2); }
Notes: Push to top of stack

## Slide 16: Recursive: Comparison
(block $B0 (br_if $B0 (i32.lt_u (local.get $p0) (i32.const 2))) (return (i32.add (call $run (i32.add (local.get $p0) (i32.const -1))) (call $run (i32.add (local.get $p0) (i32.const -2)))))) (local.get $p0)
uint32_t run(uint32_t n) { if (n < 2) { return n; } return run(n - 1) + run(n - 2); }

## Slide 17: Testcases
Recursive
Switch
Memory
Matrix Multiply
Native Calls
TypeScript
Notes: Recursive: function calls
Switch: branching in every application
Memory: no linked
Matrtix: basis for other algortihms, tight inner lop optimization
Native calls: interaction, two funcions, one with return, linked into the runtime
TypeScript: AssemblyScript subset of Typescript

## Slide 18: Evaluation
Notes: After test design compilation
Emscripten borwser => wasienv toolchain for others
Wasmc++ wraps clang++
No tail call elimination on the ESP32, but wasm3 depends on that, call frames and massive stack use => fix in sight

## Slide 19: Measurements
Test case | WASM Execution | Native Exectuion | Slowdown factor
Recursive Calls | 41,766 µs (σ=0.79) | 1,000 µs (σ=0.28) | 42
Switch statement | 1,021 µs (σ=0.71) | 0 µs (σ=0.00) | 
Memory Access | 1,802 µs (σ=0.74) | 55 µs (σ=0.26) | 33
Matrix Multiplication | 26,277 µs (σ=0.60) | 281 µs (σ=0.58) | 93
Native calls* | 33 µs (σ=5.15) | 8 µs (σ=0.64) | 4
TypeScript execution | 41,493 µs (σ=0.85) | 1,000 µs (σ=0.24) | 41
Notes: Run 100 times => average over 10
Low variance <= deterministic scheduler
* Length of ten calls
Matrix => more complex alorightms take bigher hit, contributors no expensive actions => no complex algorithms in WebAssembly
Native: little slowdown

## Slide 20: Learnings
Drawbacks
Performance loss
Significant limitations
Potential
Dynamic code
Browser execution
New languages
Notes: 30-90x slower
Unusual for webassembly
Suspect more energy => more reasearch
No malloc() only defined functions
Since common usecase => WASI for non browser platforms
Runtime => dynamic loading => meant for network
Code for embedded ion the borwser

## Slide 21: Conclusion
Notes: In summery
Runing wasm works using WASM3
40-90x slower and no interface
Performance loss but feature gain